## Slide 1: Firmware Analysis
Stephen Dunlap, CISSP
stephen.dunlap.ctr@afit.edu
This briefing, presentation, or document is for information only.
No US Government commitment to sell, loan, lease, co-develop
or co-product defense articles or provide defense services is implied or intended

## Slide 2: Controllers
Control and monitor physical components of systems
Hardware Layer
  Physical components of PLC
Firmware Layer
  Layer between the program and hardware layers
  Handles the communication between layers
  Operating System
Programming Layer
  Extra layer of abstraction
  Not always used
  Relies on firmware

## Slide 3: Goal
Modify firmware and install it on a device
Problem:
  Device will only accept vendor firmware
  Any modifications cause update to fail
Tips
  Be prepared to brick a couple devices
  Take good notes as you RE!!
  Don’t be intimidated
  Do be stubborn

## Slide 4: AB ControlLogix

## Slide 5: AB ControlLogix

## Slide 6: CubeSpace Reaction Wheel

## Slide 7: SEL RTAC

## Slide 8: SEL RTAC

## Slide 9: SEL RTAC
?
?
?
?
?
?
?
?
?
?
?
?
?
GND
?
GND
http://sun.hasenbraten.de/~frank/docs/mpc824x_JTAG.html

## Slide 10: Necessary Information
Architecture (ARM, MIPS, PowerPC)
Firmware format (compression, encryption, RTOS, FS)
Integrity checks (Checksums, CRCs, hashes, signatures)
Memory map (base address of FW, stack, heap)
Entry point (boot loader, main firmware)

## Slide 11: Step 1: Familiarization
Take pictures of the hardware
Use the device the way it was intended
Use Wireshark and nmap
Look for interesting files

## Slide 12: Step 2: Acquire Firmware
Vendor webpage
Customer support
Update utility
Extract binary image from installer
Wireshark
Hardware extraction

## Slide 13: Common Header Fields
File length
Entry point
Magic numbers
Version info
Timestamps
Memory addresses
Checksums/CRCs
Digital signatures

## Slide 14: Binary Analysis Tools
Strings
Hex Editor
Bindiff
Binwalk
Visualization
Disassemblers

## Slide 15: Binary Analysis Tools - strings
Human-readable clues
Things to look for:
  Copyrights
  Filenames
  Debug Messages
  Compiler info
  Passwords
  Keys
$ strings firmware.bin | less

## Slide 16: Binary Analysis Tools - Hex Dump
What’s in the file?
Things to look for:
  Headers/Footers
  Patterns
  Opcodes
  Container format
  Endianness
  String tables
$ hd firmware.bin | less
$ bless firmware.bin

## Slide 17: Binary Analysis Tools - vbindiff
Changes between versions
Compare minor versions
  Checksums
  Length fields
  Headers
  Version number/string
Compare major versions
  Common fields
  Length fields
$ vbindiff fw1.bin fw2.bin

## Slide 18: Binary Analysis Tools - Binwalk
Known data structures/formats
Things to look for:
  File headers
  File systems
  Compressed data
  Images
  Opcodes (-A)
  Encryption keys/certs
Beware of false positives
# Search for signatures
$ binwalk firmware.bin
# Extract nested files
$ binwalk –e firmware.bin
# Graph entropy
$ binwalk –E firmware.bin

## Slide 19: Entropy Graphs
binwalk –E toyota_sd.bin

## Slide 20: Visualization

## Slide 21: Disassemblers
Assembly
C++
Machine Code (binary)
Assembly
C++
Machine Code (binary)
Disassemble
Decompile
Assemble
Compile

## Slide 22: Questions